Specific key issues

Name of Pilot River Basin	: Lausitzer Neisse

Project leader			: Dr. Fritzsche (StUFA Bautzen)

Reporting period		: 30.09.2003

Status				: Draft

| Guidance | ToR No | Key issues | Specific question | Clarification | Suggestions for improvement |
| --- | --- | --- | --- | --- | --- |
| 2.0 Identification of Water Bodies | 2.0 - 1 | Surface Waters: Status of aquatic ecosystems in the river basin | Does the Water bodies identified permit you to provide an accurate description of the status of aquatic ecosystems in your river basin? | Define the status of aquatic ecosystems | Selecting the criteria used for water body identification we intend to be able defining the ecological status of the aquatic ecosystem in future. Actually basing on the macroinvertebrate community only the saprobic status is classified. |
| 2.0 Identification of Water Bodies | 2 | Surface Waters: Number of water bodies | How many water bodies have you identified? |  | Lausitzer Neiße (Saxony): 20 WB + major tributaries: Mandau (12 WB), Pließnitz (9 WB) => Σ 41 WB in Saxony + 2 lakes each forming a separate water body (artificial) |
| 2.0 Identification of Water Bodies | 3 | Surface Waters: Minimum size | Which is the minimum size you have identified? |  | Minimum size: 2,0 km (only Saxony considered) |
| 2.0 Identification of Water Bodies | 4 | Surface Waters: Maximum size | Which is the maximum size you have identified? |  | Maximum size: > 30 km (only Saxony considered) |

| 2.0 Identification of Water Bodies | 5 | Surface Waters: Very Small Water bodies | Which approach have you taken for very small water bodies? | How to deal with very small water bodies. | Following the ‘Horizontal guidance document on the application of the term „water body“ in the context of the Water Framework Directive’ all rivers with catchments > 10 km2 were delineated into water bodies. All the smaller ones were not considered in the reporting scale to Brussels. But also small tributaries with catchments > 10 km² were delineated into water bodies in the same way as the larger ones. As a rule a minimum size of 2 km length was defined for all water bodies. After delineation water bodies basing on equal type, pressure, and impact will be aggregated to monitoring-water body groups for each sub-basin of the main tributaries of the River Neisse and the remaining part of the River Neisse itself . |
| --- | --- | --- | --- | --- | --- |
| 2.0 Identification of Water Bodies | 6 | Surface Waters: Types | Is your typology process finalized? How many Water bodies have you identified regarding this typology? | Define types and criteria used. | In Germany there is a stream typology system with a stream type map covering the whole country. This system was used identifying the water bodies. The German stream typology uses elements of system A as well as elements of system B. The German stream type system is basing on a landscape system defined by Dr. Briem considering important hydromorphological and geochemical parameters, describing near-natural (potentially natural) conditions and the resulting aquatic community. The major parameters used, are: ecoregion, shape of the valley, slope, meandering form, stream bed substrate, hydrology, hydraulic regime, vegetation, and geochemistry. |
| 2.0 Identification of Water Bodies | 7 | Surface waters: Iterative process Information from article 5 analyses and reviews | Which problems/uncertainties have you identified? | Practicalities when implementing article 5. Uncertainties reported | Following step 4 of the horizontal guidance paper (subdivide physical divisions) we mainly used data on land utilization, results from the German river habitat survey, and data on the saprobic status. Not to get too small water bodies, which could not be managed in future, we tried to aggregate the data to classes and we summarized neighbouring reasons for water body identification by selecting the most important reason. This was necessary because of very local changes in land utilization and morphological structure (=> German habitat survey). We aim to define water bodies as homogenous as possible, but in most cases not smaller than 4 km (never < 2 km). In general we conclude: the larger the river is, the larger also should be the water body. |
| 2.0 Identification of Water Bodies | 8 | Surface waters: Review of the water bodies identification process | Will you review the water bodies identification following the article 5 analysis or after the establishment of the monitoring programme? | Revision after the fulfillment of article 5 requirements or after the monitoring. | We believe that it will be necessary to review the water bodies identification following the article 5 analysis as well as after the establishment of the monitoring programme. |
| 2.0 Identification of Water Bodies | 9 | Surface waters: Pristine waters | Have you identified water bodies with pristine waters? |  | In the River Basin of the Lausitzer Neisse there is no natural region, which can be used as reference. So we used the stream type definition of the German stream type system as reference and scale for assessment. So we don‘t have water bodies with reference conditions. Information on the definition of reference conditions, see 2.3.6. |
| 2.0 Identification of Water Bodies | 10 | Surface Waters: Status of aquatic ecosystems in the river basin | Does the Water bodies identified permit you to provide an accurate description of the status of aquatic ecosystems in your river basin? | Define the status of aquatic ecosystems Please provide indication on the average quality of status. | See Question 1) Preliminary information on the ecological status of the water body are given by the saprobic status. The assessment system using 7 saprobic classes must be transfered to the WFD classification system using 5 classes and it was adapted to the specific stream type conditions. (Research project: ‚Entwicklung eines leitbildorientierten Saprobienindexes für die biologische Fließgewässerbewertung’; UBA 2003; Forschungs-vorhaben 20024227). |
| 2.0 Identification of Water Bodies | 11 | Surface waters: Aggregation of water bodies | Which criteria have you applied when aggregating water bodies? |  | We aggregate water bodies to groups when they are homogeneous concerning type, pressure and impact and belong to the same sub-basin. See also Question 5)) |
| 2.0 Identification of Water Bodies | 12 | Surface waters: Sub-division of water bodies | How have you considered sub-division and which criteria have you used? |  | If a water body is not really homogenous in its pressures and impacts and a delineation into separate water bodies would result in one or more water bodies of significantly less than 2 km, we divided this water body into homogenous sub-water bodies to keep the information for the management program while avoiding the delineation of too small waterbodies. Also in transboundary catchments we subdivide water bodies, delineated according to the horizontal guidance document into sub-water-bodies using the frontier line for seperation. We believe this as necessary because by subdividing the water body, measures will be harmonized between the different countries but in realizing measures every country will be responsible for its own sub-water body. (=> considering national autonomy). |
| 2.0 Identification of Water Bodies | 13 | Surface waters: Physical features | Which physical (geographical and hydromorphological) features have you used when identifying discrete elements of surface water bodies? |  | Separating categories (GIS): River and lake shape (Saxony); Stream types: German stream type shape (Saxony); Major tributaries: DLM 1000 W; Additional criteria: German habitat survey, saprobic status, land utilization (Saxony) |
| 2.0 Identification of Water Bodies | 14 | Surface waters: Protected areas | How have you considered protected areas (e.g. Natura sites, or drinking water sources)? |  | FFH-areas were considered. Smaller natural reserves and protection areas were ignored. |
| 2.0 Identification of Water Bodies | 15 | Surface waters: Wetlands associated to water bodies | Have you considered wetlands associated to your water bodies? How have you considered the relationship? | Wetlands related to surface waters. | Wetlands were not considered. |
| 2.0 Identification of Water Bodies | 16 | Ground Waters: Number of water bodies | How many water bodies have you identified? |  | 5 ground water bodies |
| 2.0 Identification of Water Bodies | 17 | Ground Waters: Minimum size | Which is the minimum size you have identified? |  | Minimum size: 24 km² |
| 2.0 Identification of Water Bodies | 18 | Ground Waters: Maximum size | Which is the maximum size you have identified? |  | Maximum size: 557 km² |
| 2.0 Identification of Water Bodies | 19 | Ground Waters: Very Small Water bodies | Which approach have you taken for very small ground water bodies? | How to deal with very small water bodies. | - |
| 2.0 Identification of Water Bodies | 20 | Ground waters: Significant flow in aquifers | When designating groundwater bodies, how have you considered “significant flow”? |  | - |
| 2.0 Identification of Water Bodies | 21 | Ground waters: Delineation of groundwater bodies | Which criteria have you used when identifying and delineating groundwater bodies? |  | - |
| 2.0 Identification of Water Bodies | 22 | Ground waters: Groundwater boundaries | How have you identified boundaries of groundwater? |  | - |
| 2.0 Identification of Water Bodies | 23 | Ground waters: Wetlands associated to water bodies | Have you considered wetlands associated to your ground water bodies? How have you considered the relationship? | Wetlands related to ground waters | - |
| 2.0 Identification of Water Bodies | 24 | General issues: Local and regional circumstances | Which local and regional circumstances have you considered when identifying water bodies?. How have you done it? |  | The national frontier is only a criteria for separating sub-water bodies but not water bodies. |
| 2.0 Identification of Water Bodies | 25 | General issues: Recommendations General issues to raise Experience | Which general problems/experiences/recommendations have you encountered when identifying water bodies in your river basin? | General Comments and Suggestions | Following the guidance-papers the results may be different depending on the person using it, because in these papers a wide scale of interpretation is possible. The results are also depending on the data available. Also following different strategies in identifying water bodies we hope that the results will be comparable at the end. In the PRB Lausitzer Neisse we have the problem of a catchment belonging to three different states (Czech Republic, Poland, Germany) with the frontiers defining the boarders of the water bodies. |

1) ref. 2.0 Identification of Water Bodies (Surface Waters: Types)

LAWA-Stream types in the Lausitzer Neisse basin (Saxony)

Types in the mountainous region

Type 5: brooks in siliceous mountainous region (s)

Type 9: mid-sized stream in siliceous mountainous region (s)

Type 9.2: large river in siliceous mountainous region (k)

Types in the lowland area of northern Germany

Type 14: sandy lowland brooks (s, k)

Type 15: lowland mid-sized stream characterized by sand and clay  (k)

Type 16: lowland brooks with gravel (s, k)

Types, not depending on ecoregion

Type 11: brooks with organic streambed (bog, moor, swamp) (o)

Type 19: stream in the broad river valley (k)

| Guidance | ToR No | Key issues | Specific question | Clarification | Suggestions for improvement |
| --- | --- | --- | --- | --- | --- |
| 2.1 Pressures and impacts | 2.1-1 | Criteria for (potential) significant pressures | Is the list of “pressures” and the related “criteria” adequate as a basis to define those significant pressures at water body level that pose a risk of failing to meet the environmental objectives | A qualifier or a set of qualifiers (in this case “pressures” and related “criteria”) can be used as such (independent of the specific water body). The question is whether the applied qualifiers are a useful tool to decide whether the specific water body (management unit) will reach or fail the good status. | The list of pressures in the IMPRESS guidance document is rather detailed. Using every parameter mentioned there would need a big data set. The German LAWA published a „criteria document“ to identify significant pressures in a more easy way. This document is also mentioned in the IMPRESS paper as a possible tool, helping to do the pressure and impact analysis in time. In the PRB Neisse we considered these LAWA criteria as well as some additional parameters important in this catchment: We assume, that non point sources of nutrient input will play an important role in the Neisse basin because of agriculture being the major land utilization there. Using results from an other research project, detailed data from water balance models are available. Combining these data with the results of nutrient wash out calculated by MONERIS we are able to estimate the relative load of non point sources. We will compare these results with the assessment of the LAWA „criteria document“. |
|  | 2.1-2 | Impact indicators and their thresholds | Is the list of “impact indicators” and “threshold sizes” adequate to asses the risk of failing to meet the environmental objectives | A qualifier or a set of qualifiers (in this case “impact indicators” and related “thresholds”) can be used as such (independent of the specific water body). The question is whether the applied qualifiers are a useful tool to decide whether the specific water body (management unit) will reach or fail the good status. | In the LAWA „criteria document“ used (see 2.1-1), the way how to identify significant pressures as well as criteria for impact indicators for chemical pollution and corresponding thresholds are described there. |
|  | 2.1-3 | DPSI(R) concept | Is the DPSI(R) concept applicable in practice | How are the experiences with the (P)ressures – (S)tate-(I)mpact relation (in fact what is the relation between the P (pollution source or activity) – S (the measured state in the water body) and the I (can objectives be met). Which models were used? How was it done in case of hydro morphological changes? Role of expert judgements etc. | The relation between pressures and state variables not assessed (following the DPSI-concept called „state“, e.g. O2-concentration, HQ1, etc.) can be modelized rather easily. Models normally used are: precipitation-discharge-models or water balance models (e.g. NASIM), water quality models (e.g. ATV-FGSM) and models calculating the emission rate (emission model for urban areas e.g. MONERIS calculating the emission of non point sources, see 2.1-1). We think that it is unlucky to use the word „state“ (= not assessed) because it is easy mixed with the word „status“ (e.g. ecological status) assessing the state. And it is not clear how to separate „status“ from „impact“. |
| 2.3 REFCOND | 2.3-1 | Availability of an infrastructure | 1. Please give information on the availability of an infra structure consisting of: Expertise Databases Models and other tools Organisational structure 2. If the infrastructure was not (sufficiently) available, have you set up a group of experts for matters related to reference conditions and classification, ecological, chemical, hydrological, and statistical expertise as well as expertise on modelling, GIS and databases? | Databases are needed for the identification of relevant water bodies and characterisation of pressure and state. State variables would be those required in the WFD for characterisation and classification of water bodies (Annex II and V) plus optional variables suggested in the WFD or other variables preferred by MSs. Pressure variables would include measures of land-use, point source discharges, hydro morphological alterations, etc. It should be stressed that without access to data, an orderly implementation of the WFD is impossible. | see 2.0-13 and Meta-Database (not included but part of the progress report) |
|  | 2.3-2 | Differentiation of a water body type | Did you use “system A” or “system B” in differentiating the surface water body types? Did you apply the obligatory factors of “system A” in case you chose “system B” ? |  | See 2.0-6 |
|  | 2.3-6 | Validation | Are reference conditions and ecological class boundaries validated |  | Reference conditions are describing the situation of water bodies not or only poor influenced by human activities. Though they are useful, more or less uninfluenced natural streams are rather rare and only a few of the 23 German stream types are represented by an existing reference stream. So in Germany reference conditions are mostly constructions of potential natural conditions. The reference conditions for every stream type are characterized by a checking list, with not always a really existing stream as example. These checking lists are actually revised. The final definition and description of the 5 quality classes (from „high“ to „bad“) for all biological quality elements isn‘t finished yet in Germany. But there are already some assessment methods proposed, basing on different research projects (e.g. AQEM (The development and testing of an integrated assessment system for the ecological quality of streams and rivers throughout Europe using benthic macroinvertebrates ) = multimetric index, assessing the saprobic status and morphological degradation). Conclusion: In Germany reference conditions as well as the 5 ecological quality classes are not finally defined and validated. Nevertheless it is possible to use these preliminary results without expecting a complete revision of the methods and results. |

# Text boxes

Working team IPS & ube (contractors of the StUFA-Bautzen):

Dr. Sieker (Ingenieurgesellschaft Prof Sieker: IPS) and

M. Halle, Dr. Podraza, & S. Seuter (umweltbüro essen: ube)