Pilot River Basin Lausitzer Neisse

Watershed Characteristics

Project Coordinator:	Dr. B. Fritzsche, Stufa Bautzen

Consulting Team 	Ingenieurgesellschaft Prof. Dr. Sieker mbH (IPS) 
& umweltbüro essen (ube)

# Catchment location and size

The Lausitzer Neisse basin is part of the Odra catchment. The river has its source in the Czech Republic near the city of Liberec in a height of 785 m+NN. After flowing approx. 50 km through the Czech republic with a mean slope of 1% it crosses the border to Germany and Poland.

For the following 300 km until flowing into the Odra the Neisse forms the borderline between Germany and Poland. The mean slope is approx. 0.1%

Total catchment size is approx. 4.400 km² whereof about 50% belong to Poland, 30% to Germany and 20% to the Czech Republic.

Fig. 1:	Location of the Neisse catchment

# Topography

The spring of the river Neisse is in a height of 785 m+NN. At the mouth to the Odra the elevation is 41m+NN.

Fig. 2: Relief of the Neisse catchment

# Climate

The mean annual precipitation is between 600 and 800 mm.

# Geomorphology

The upper part of the basin is assigned to the ecoregion ‘central highland’, the lower part to the ecoregion ‘central lowland’.

Geology in the catchment consists predominantly of Rumburger granite and Granodiorit. The relief is stamped by glacial conditions. A typical soil type is loess. See Fig. 2 for an example of the soil type map of Saxony.

Fig. 3:	Section of the soil type map of Saxony

# Land use

So far only information about the Saxonian part of the catchment can be presented here.

Fig. 4:	Land use in the saxonian part of the Neisse catchment